## Slide 1: Cell Therapy for Spinal Cord Injuries: Commercial Manufacturing Facility
Rebecca J. Carlson and Ariel M. Rose
Chemical Engineering & Materials Science Michigan State University

## Slide 2: Introduction
250,000 people in the US and over 440,000 people in Europe have a spinal cord injury (SCI)
Estimated lifetime costs per person are 1-5 million dollars
Goal: Produce neural stem cells (NSCs) for treatment of spinal cord injuries (SCIs)
  Production in US with possible expansion to Europe
National Spinal Cord Injury Statistical Center. (2012). Spinal cord injury facts and figures at a glance.

## Slide 3: Proposed Timeline
10 years
US and Europe production
(5,500 doses/yr)
1 year
Phase III clinical trials (1,500 doses)
10 years
US production
(3,000 doses/yr)
2 years
Phase I/II clinical trials
Facility construction
Notes: REMEMBER: mention 3000 doses/yr by determining fraction of people in the US likely to want/need the therapy

## Slide 4
Use of adult stem cell inoculum per problem statement
  Mesenchymal cells (MSCs) differentiated to neural stem cells (NSCs)
    No ethical issues
    May be used for allogeneic transplantation
Ethically Appropriate
High Quality
Economically Competitive

## Slide 5
Quality Inspection
of Intermediate and Final Cell Cultures
            Identity – surface markers
            Purity – detect viruses, bacteria
            Potency – verify differentiation
            Viability
            Cell number
            Biocompatibility
Safety: Layers of quality control
Quality inspection
cGMP-certified equipment and materials
Cells
Liquids
Disposable Reactors, Microcarriers
Procurement
Validation
Raw Materials
Equipment
Cell Samples
Microcarriers
Procedural Controls
Autoclaving
Aseptic handling
Disposable bioreactors
Controlled disposal systems
Virus filtration
Ethically Appropriate
High Quality
Economically Competitive
Notes: Unidirectional flow, total 5045 ft2, reasonable size for facility with this number of treatments
Viruses with immunochromatographic test stripes, endotoxin with LAL assay, Gram stains, hemagglutination, cytopathic effects

## Slide 6
Safety: Proposed cGMP Facility Layout
Ethically Appropriate
High Quality
Economically Competitive
Notes: Unidirectional flow, total 5045 ft2, reasonable size for facility with this number of treatments

## Slide 7
Ethically Appropriate
High Quality
Economically Competitive
ThawSTAR® system standardizes thawing
Notes: Expansion lasts:

## Slide 8
Ethically Appropriate
High Quality
Economically Competitive
All inputs cGMP-certified
Serum-free, xeno-free materials
Filtration
Notes: Expansion lasts:

## Slide 9
Pall SoloHill Plastic Plus optimal microcarrier
        Non-xenogeneic
        Withstand autoclaving
        Relatively inexpensive
        High cell attachment (even in FBS-free media)
        Lack of micropores allows easy detachment
        Available in small diameters
          Cells experience minimal shear force as long as Kolmogorov eddy length >1/2Dmicrocarrier
http://ru.pall.com/main/biopharmaceuticals/bioprocess-vision-issue.page
Ethically Appropriate
High Quality
Economically Competitive
Notes: http://ru.pall.com/main/biopharmaceuticals/bioprocess-vision-issue.page
Dmicrocarrier is 120um, verified Kolmogorov at least 60um for all runs

## Slide 10
Ethically Appropriate
High Quality
Economically Competitive
PBS Biotech Vertical Wheel Bioreactor
  Vertical wheel minimizes shear stress
  Already optimized for MSC culture
  Scalable
  Accommodates microcarriers
Bioreactor conditions
  Higher proliferation under hypoxic conditions
  Differentiate with EGF and FGF2 growth factors
  Better differentiation at 32°C
  Passage by detaching cells from microcarriers at high agitation
  Final separation: xeno-free trypsinization
http://www.pbsbiotech.com/pbs-3.html
Notes: Do we want to talk more about detachment?
Expansion lasts: 10 days in T75, 7 days each in 0.1 L, 0.5 L, 3, 15, and 80 L reactors
3 parallel trains up to and including 0.5 L in case of contamination or subpar growth
Assume exponential growth, doubling time of 62.4 hours in bioreactors, 200hrs in T75 flasks

## Slide 11
Bioreactor Performance
    Shear stress:
        All calculated less than 4 dyn/cm2, MSC differentiation not induced until 15 dyn/cm2
    Mixing time:
        All mixing times under 17s
Ethically Appropriate
High Quality
Economically Competitive
Notes: http://ru.pall.com/main/biopharmaceuticals/bioprocess-vision-issue.page
Nu kinematic viscosity believe used paper, epsilon is power per unit mass

## Slide 12
Bioreactor Performance
    Oxygen mass transfer:
        Calculated maximum viable cell density greater than actual in all cases
Ethically Appropriate
High Quality
Economically Competitive
Notes: Sour is g o2/cell/hr
Otr = g o2/l/hr

## Slide 13
Ethically Appropriate
High Quality
Economically Competitive
Fluidized bed centrifugation removes microcarriers, washes, and concentrates cells in one step

## Slide 14
Ethically Appropriate
High Quality
Economically Competitive
Magnetic-activated cell sorting (MACS):
High-throughput
Low-cost
Low processing times
Does not require single-cell suspension
Notes: Low processing of 3 hrs relative to FACS but yield only about 60%. Low processing increases recovery, viability.

## Slide 15
Ethically Appropriate
High Quality
Economically Competitive
Negative Selection with MACS Separation
Labeled cells: Undifferentiated MSCs (CD166hi, CD44hi, CD105hi)
Unlabeled cells: NSCs
Notes: Low processing of 3 hrs relative to FACS but yield only about 60%. Low processing increases recovery, viability.

## Slide 16
Ethically Appropriate
High Quality
Economically Competitive
Labeling and freezing:
Vials with pre-labeled barcodes
Automatic vial filler
Controlled rate freezing
Notes: Fill it vial filler, 10% DMSO

## Slide 17
Chart: 
| ThawStar® | Bioreactors | kSep Centrifugation | CliniMACS® Plus | Product Finishing and Shipment | Tissue Culture | Quality Control | Cold Storage | Additional Equipment
ThawStar® Bioreactors PBS 0.1 MAG PBS 0.5 MAG PBS 3 MAG PBS 15 MAG PBS 80 MAG kSep Centrifugation Chiller FBC Equipment Steel bench Bag holder tray Welder for sterile tubing connections Skid cost CliniMACS® Plus Product Finishing and Shipment Sartori | 7180 | 722173.08 | 219548 | 64900 | 149187.5 | 120266.82 | 171038 | 66681.51 | 580482.07
Equipment and Fixed Capital Investment
Estimated equipment cost - $2.1M ($1.51M average for same-size facility)
  Majority of cost from bioreactors, additional equipment (mainly tanks), kSep centrifugation
Total capital cost - $36M, working capital is $7.2M
Ethically Appropriate
High Quality
Economically Competitive
Notes: Additional: filter integrity tester, autoclave, waste tanks, vessels for media and buffer preparation

## Slide 18
Manufacturing Costs
$32.1M/yr for US operations, direct cost of $5,380/dose (compared to estimate of $1,890 in literature)
Chart: 
| Labor | Raw Materials | Reagents | Disposable Equipment | Electricity | Other Utilties | Other Fixed Costs | Depreciation
Manufacturing | 4799609.2998 | 40380 | 10415503.9583 | 837781.5128 | 37061.7567 | 4466.5196 | 12233953.187 | 3772814.2237
Ethically Appropriate
High Quality
Economically Competitive
Notes: Additional: filter integrity tester, autoclave, waste tanks, vessels for media and buffer preparation

## Slide 19
Profitability
Used MACRS depreciation rates, took into account cost of clinical trials
Suggested $40,000/dose (low compared to suggested price of $500,000 for cell therapies at this scale)
 | US Project | US and European Project
IRR | 55.99% | 56.23%
Net Present Worth (NPW) | $553,960,000 | $1,726,990,000
Price per Dose Yielding 50% IRR | $35,364 | $34,975
Ethically Appropriate
High Quality
Economically Competitive
Notes: Expansion to Europe likely not worth it unless done earlier (equipment replacement at 10years). Also not considered here is simply obsolence of technology

## Slide 20
Sensitivity Analysis
Chart: Parameter Varied
| Proliferation Media | Labor | Working Capital | Clinical Trials | Equipment | Fixed Manufacturing
 | -1.4293 | -0.72961 | -0.62962 | -0.41154 | -4.132 | -1.3271
Ethically Appropriate
High Quality
Economically Competitive
Notes: A sensitivity analysis was performed on six key process costs (Figure 25, detailed results in Appendix M). Based on the analysis, changes in fixed equipment cost had the larges impact on net present worth, largely due to the many multipliers that result in an estimate of total fixed capital investment as a function of the equipment purchased cost. Next, the percentage change in proliferation media cost and the fixed manufacturing costs had a large effect on NPW. This means that, since the price used for the media was not a bulk estimate, the NPW is likely much higher than estimated in the report. Fortunately, although the cost for clinical trials was only an approximate estimate, percentage changes in this cost have a fairly small effect on NPW.

## Slide 21
Chart: Media Change Frequency (hr)
| 2 | 4-2 | 8-4-2 | 12-8-4-2 | 24-12-8-4-2
 | 54388.6914 | 41664.8051 | 37697.0146 | 36628.989 | 36254.4417
Optimization
Media change frequency – at maximum cell density, must change every 2 hours
Ethically Appropriate
High Quality
Economically Competitive
Notes: Additional: filter integrity tester, autoclave, waste tanks, vessels for media and buffer preparation

## Slide 22
Optimization
Optimization Step | Yearly Savings | % ROI Savings | Cumulative % ROI Savings
Prelabeled tubes | NA | 2.5% | 2.52%
PBS buffer formulation onsite | $5,210 | 0.02% | 2.54%
Proliferation media selection | $13,209,000 | 22.8% | 25.3%
Media change frequency | $4,479,000 | 12.7% | 38.0%
Ethically Appropriate
High Quality
Economically Competitive
Notes: Additional: filter integrity tester, autoclave, waste tanks, vessels for media and buffer preparation

## Slide 23
Other Optimizations Considered
Tangential Flow Filtration – cheaper than FBC for processes at similar number of doses, cells/dose
  Device from Lonza not yet available for purchase commercially
Liquid Nitrogen Generation Onsite – 3.9% ROI loss
  Could be reconsidered with more precise LN2 consumption estimates
Ethically Appropriate
High Quality
Economically Competitive
Notes: Additional: filter integrity tester, autoclave, waste tanks, vessels for media and buffer preparation

## Slide 24: Conclusions and Recommendations
Cell Therapy Process
Achieved 3 Key Objectives:
Future Recommendations
Further study of novel therapy
  Client base
  Efficacy
  Growth Dynamics
  Differentiation Efficiency
  Business Model
Target identified losses
Chart: 
| Not viable | Undifferentiated | Lost in FBC | Lost in CliniMACS | Lost due to sampling | Lost due to DMSO/Freezing | Lost due to extra cells
 | 31150881330.9974 | 126693749461.2995 | 30732836503.5354 | 49172538405.6567 | 3687940380.4243 | 19619842823.857 | 11642544093.2778
Ethically
Appropriate
High Quality
Economically Competitive
Cell Losses

## Slide 25
Acknowledgments
Industry representatives (time, resources, expertise)
Michigan State University Chemical Engineering and Materials Science department (training, support)
God and family (sustenance and encouragement)

## Slide 26
Questions?